## Slide 1
METHOD WALKTHROUGH · 18 SEPTEMBER 2026
BPP + iPhUMI, step by step
One handheld demonstration in,
robot actions out — no weight updates
Behavior Prompting Policy (Patel, Pekarek, Castro Hernandez & Song, Stanford, 2026) applied to the Unitree G1 cup task
Record → build prompt → match the eyes → infer → execute → swap prompt → (train if needed) → evaluate
Sources: arXiv:2606.30457 · github.com/real-stanford/behavior_prompting · github.com/real-stanford/iPhUMI · MIT licence
Notes: Standalone walkthrough of the BPP + iPhUMI route from the team deck. Numbers are from the paper (arXiv:2606.30457) and the repos; G1-specific values are proposals to validate, not measured results.

## Slide 2
OVERVIEW
What BPP + iPhUMI is, in one picture
BPP + iPhUMI on the Unitree G1 · step by step
02 / 15
iPhUMI demo
wrist RGB · 6-DoF pose · width
Prompt chunks
1 Hz obs + full-rate actions
Prompt encoder
cross-attention to live obs
Action decoder
diffusion U-Net
Action chunk
Δpose + gripper width
The prompt
A single demonstration of the task in a different scene layout: a sequence of observations, proprioception and actions in the same sensorimotor space the robot executes in. It says what the task is and shows one way to do it.
The policy
Prompt encoder (6-layer transformer decoder, ~57M params) extracts the relevant part of the prompt for the current observation; a CNN U-Net diffusion decoder (~151M) denoises an action chunk. Weights frozen at test time.
The interface
iPhUMI: UMI gripper with an iPhone 15 Pro instead of a GoPro. ARKit SLAM gives instant 6-DoF localisation with no mapping step, and the app sends a demo wirelessly to the policy at test time.
Same weights, different demo → different behaviour. That is the whole claim we will test on the G1.
Notes: BPP is a diffusion policy with one extra input: a behavior prompt, a single demonstration in the robot's own sensorimotor space. iPhUMI is the handheld UMI-style gripper with an iPhone that records exactly that. The weights stay frozen; only the prompt changes.

## Slide 3
SETUP
What you need on the bench before step 1
BPP + iPhUMI on the Unitree G1 · step by step
03 / 15
iPhUMI (handheld, no robot)
• 3D-printed UMI-style gripper with an iPhone 15 Pro mount and ArUco tags on the fingers
• Open-source iOS app: records main camera 1920×1440 @ 60 Hz, ultrawide 640×480 @ 10 Hz, LiDAR depth, 6-DoF pose @ 60 Hz, gripper width @ 10 Hz
• Export via USB-C to SD card, or wireless transfer in prompting mode
• Optional: contact microphone, bimanual and head-mounted phones sharing one ARKit frame
Unitree G1 side (proposed)
• Parallel gripper on one arm; hand width calibrated to the same [0,1] scalar as iPhUMI
• iPhone (or camera at the identical iPhUMI offset) mounted on the gripper, streamed 960×720 @ 60 Hz over USB/Ethernet using the iPhUMI deployment mode
• Workstation GPU running the policy server; G1 gateway owns IK, limits and actuation
• Calibrated wrist-to-TCP and gripper geometry (guide Sections 7–9)
Item | Why it matters
Wrist-camera offset matches iPhUMI | The policy's visual prior is tied to where the camera sits relative to the fingers
Gripper width scalar matches | Actions carry a width command; mismatch means wrong grasp timing
Relative end-effector actions | BPP outputs UMI-style Δpose; the gateway must integrate them from the measured TCP
Same task family in training data | BPP recombines known primitives; a cup body-grasp must exist in training
Notes: Two devices: the handheld iPhUMI for recording prompts and training data, and a matched wrist camera on the G1's parallel gripper. The G1 side is our proposal; the paper deploys on an ARX arm and a bimanual setup.

## Slide 4
STEP 1
Record the prompt with iPhUMI — no robot involved
BPP + iPhUMI on the Unitree G1 · step by step
04 / 15
1
Pick up the gripper, tap record, do cup → coaster once, stop.
iPhUMI recording (one demo, ~8 s)
main camera 1920x1440 @ 60 Hz wrist view
ultrawide 640x480 @ 10 Hz context
gripper pose 6-DoF @ 60 Hz ARKit SLAM, world frame
gripper width scalar @ 10 Hz ArUco tags on fingers
task label "cup_to_coaster" typed or spoken (speech-to-text)
Before the first demo
• Calibrate gripper width once (~10 s open/close clip)
• Start the app; ARKit initialises a world frame — no mapping walk
• Use a scene layout that differs from the test scene
• Review the clip in the app; swipe to delete bad takes
Output of step 1: one exported demo folder (videos, pose log, width log, label). Nothing has been trained; the robot has not moved.
Held-out prompts for the final evaluation are recorded only after the pipeline is frozen, and are never used to train weights or tune retrieval.
Notes: One-time gripper calibration first: ~10 s clip opening and closing the gripper in calibration mode; the ultrawide camera reads the finger ArUco tags to learn min/max width. Then demonstrate cup → coaster once in a different scene layout than the test.

## Slide 5
STEP 2
Turn the recording into a behavior prompt
BPP + iPhUMI on the Unitree G1 · step by step
05 / 15
2
Convert to sensorimotor data, then chunk and pool.
per step t:
o_t wrist RGB frame
q_t EE pose + gripper width
a_t relative EE pose to next step + width
chunks (obs/proprio ~1 Hz, actions full rate):
chunk_0 = { o_0.0s, q_0.0s, [a_0.00 ... a_0.95] }
chunk_1 = { o_1.0s, q_1.0s, [a_1.00 ... a_1.95] }
...
chunk_7 = { o_7.0s, q_7.0s, [a_7.00 ... a_7.95] } release
attention pooling: {o,q,a} -> p_i
P = [p_0, p_1, ..., p_7] cached once per rollout
Why this format
• Observations anchor the prompt lookup ("where am I in the task")
• Actions give temporal transitions between the sparse frames
• Pooling halves the sequence length and ties modalities from the same instant together
• Computed once per rollout, so prompt cost is paid up front, not per control step
Output of step 2: P, a short sequence of chunk embeddings. The same code path is used for training demos and for test-time prompts.
Notes: Observations and proprioception are downsampled to about 1 Hz for compute; actions are kept at full rate so the motion is complete. Each chunk = one observation + proprio + the Δt actions up to the next chunk, attention-pooled into a single embedding. Ablations: aggressive downsampling below 1 Hz hurts; including actions helps; attention pooling beats separate per-modality tokens.

## Slide 6
STEP 3
Put the same eyes and hand on the G1
BPP + iPhUMI on the Unitree G1 · step by step
06 / 15
3
Make the live observation look like the prompt.
Signal | iPhUMI (prompt) | G1 (live) | Check before motion
Wrist RGB | iPhone main camera on the UMI mount | iPhone or matched camera on the gripper, 960×720 @ 60 Hz stream | Overlay a still cup from both devices at the same TCP pose
EE pose | ARKit 6-DoF in world frame | Measured TCP from FK in base frame | Round-trip pose through the codec within tolerance
Gripper width | ArUco-calibrated [min,max] → scalar | Hand synergy calibrated to the same scalar | Command 0 / 0.5 / 1 and measure finger gap
Action | Relative EE pose + width, UMI convention | Δpose integrated from measured TCP, then IK in the gateway | Identity action → no motion; +x moves along observed TCP x
Output of step 3: a live observation stream in the prompt's format, and a passed codec sign test. No neural action has been executed yet.
If the released checkpoint's camera or gripper cannot be matched, step 7 (train on our own iPhUMI data) becomes mandatory rather than optional.
Notes: The policy only works if the live observation has the same form as the prompt: same camera placement relative to the fingers, same width scalar, same action convention. This is the transfer risk for the G1 and should be validated with codec tests before any powered motion.

## Slide 7
STEP 4
Inference at one control step
BPP + iPhUMI on the Unitree G1 · step by step
07 / 15
4
INPUT = P (cached) + current wrist frame, EE pose, width → OUTPUT = action chunk
Prompt chunks P
cached per rollout
Prompt encoder
cross-attention: what part of the demo matches now?
Action decoder
diffusion U-Net, K denoising steps
Action chunk
e.g. 16 × [Δx Δy Δz Δrx Δry Δrz g]
current observation
(wrist RGB, EE pose, width)
What the attention does
On tabletop tasks the prompt encoder's attention tracks discrete milestones — next object to touch, where to place — rather than every frame. On drawing tasks it tracks the demo continuously. Either way BPP adapts by dense sub-goal conditioning on the prompt.
Output of step 4: a short chunk of relative end-effector targets plus a width command, in the prompt's action convention.
Notes: Prompt encoder: transformer decoder, 6 layers, hidden 768, 8 heads, ~57M params; current observation tokens (one per entry per history step) cross-attend to the prompt chunks with learned positional embeddings. Action decoder: CNN U-Net diffusion with FiLM, down dims [256,512,1024], kernel 5, ~151M params. Prompt information is extracted once per inference step, then many denoising steps run without touching the prompt.

## Slide 8
STEP 5
Execute through the G1 gateway and re-observe
BPP + iPhUMI on the Unitree G1 · step by step
08 / 15
5
Closed loop: execute a prefix, observe again, infer again — same P every time.
Integrate
T_target = T_observed · ΔT per step of the chunk
Validate
Reject NaN, stale, unreachable or colliding targets — never clip
IK + limits
Regularise toward the measured configuration; joint and velocity limits
Execute prefix
Run the first few steps at the policy rate; hold the command lease
Re-observe
New wrist frame + TCP + width → back to step 4
Timing item | Proposed value | Note
Policy rate | 10 Hz | Must match the training time step; revisit after profiling
Prompt encoding | Once per rollout | Cached chunk embeddings; not on the per-step path
Chunk execution | Short prefix, then replan | No blending unless the pose representation is stated and validated
Latency budget | Capture → accepted target, p50 / p95 / max | Log deadline misses; abort on stale observations
Notes: The policy never talks to actuators. The gateway integrates the relative targets from the measured TCP, solves IK with joint and velocity limits, checks reach and collision, executes a short prefix of the chunk, then the loop re-observes and re-infers with the same cached prompt.

## Slide 9
STEP 6
Swap the prompt: the two-cup test
BPP + iPhUMI on the Unitree G1 · step by step
09 / 15
6
Record bowl → mug, rebuild P, run again. Same weights, same scene, different behaviour.
run A: INPUT = P_cup_to_coaster + live obs -> actions toward the cup, then the coaster
run B: INPUT = P_bowl_to_mug + live obs -> actions toward the bowl, then the mug
weights: identical (hash-checked) scene: identical prompt: differs
Condition | Prompt | Expected if ICL is real | Failure it exposes
Correct prompt | Demo of the requested outcome | Requested cup and destination | —
No prompt | Empty / zero context | Degraded or default behaviour | Task learned into the weights
Wrong-task prompt | Demo of the other outcome | Follows the wrong demo, not the nearest object | Prompt ignored
Shuffled prompt | Chunks in random order | Degraded | Temporal structure unused
Retrieved prompt | Nearest legal demo by task + initial scene | ≈ correct prompt | Retrieval leakage
Specify where prompt demos come from: matched scene layout vs unmatched. Matching cup identity by appearance across scenes is a harder, separate claim — report it as its own row.
Notes: This is the experiment that separates in-context learning from a policy that has simply learned the cup task. Same weights, same scene, two candidate outcomes visible; only the demonstration changes. A policy that always picks the nearest cup has not passed. Wrong-prompt stress tests run in simulation first.

## Slide 10
STEP 7 (IF NEEDED)
Train BPP on our own iPhUMI data
BPP + iPhUMI on the Unitree G1 · step by step
10 / 15
7
Only if the released checkpoint does not grasp our cup, or the camera/gripper cannot be matched.
for each training step:
task <- sample a task group
prompt <- one demo of task # different scene layout
batch <- (obs history, future actions) from OTHER demos of task
loss <- diffusion loss on predicted action chunk | prompt, obs
never: same episode as prompt and query; never: query's future labels in context
Data recipe (paper)
• Task diversity beats demos-per-task at a fixed budget
• Real drawing: 200 human tasks × 5 demos (iPhUMI) + 800 scripted tasks × 6 demos
• Laundry: ~150 demos/task + ~1,000 corrections — and BPP conditioned weakly there
• Split by task and session, never by frame
Setting (paper) | Value
Prompt encoder | 6 layers · hidden 768 · MLP 3072 · 8 heads · 57M params
Action decoder | CNN U-Net · step-emb 128 · down dims [256, 512, 1024] · kernel 5 · 151M params
Compute per benchmark | 24–42 h on 4× L40S / A6000 (DDP), including rollout evaluations
Prompt downsampling | Obs/proprio ~1 Hz; actions full rate; attention pooling per chunk
Notes: Training is standard diffusion-policy behaviour cloning with one extra input. Each step: sample one demo as the prompt, then a batch of receding-horizon observations and future action chunks from other demos of the same task. No spatial or temporal correspondence labels are needed. Task groupings define what a prompt can control: two grasp strategies for one object must be two task groups.

## Slide 11
STEP 7 (IF NEEDED)
What we would collect for the cup task
BPP + iPhUMI on the Unitree G1 · step by step
11 / 15
Phase 1 · pilot
6 task variants × 20 demos + 2 dev variants × 10, all with iPhUMI. Purpose: converter, codec, splits and training loop. Not expected to show context use.
Phase 2 · diversity
Dozens of variants: cup × destination × approach × lighting × distractors, 5 demos each. Add scripted or simulated variants (Instant Policy / SynthICL style) to reach hundreds of task groups.
Held-out
Prompt demos for evaluation recorded after the pipeline is frozen; never used for weights or retrieval tuning. Two-cup conditions with both matched and unmatched prompt scenes.
Task group example | What the prompt should control
cup_to_coaster / cup_to_tray / cup_to_shelf | Destination
cup_left / cup_right (two identical cups) | Which object
body_grasp / rim_grasp (later phase) | Grasp strategy — must be separate groups
approach_front / approach_side | Motion plan
Rule from the paper: the granularity of task groups is the granularity at which a prompt can change behaviour.
Notes: BPP's own limitation section: substantial training-task diversity is required, and weak task conditioning appears when diversity is low. So the collection plan is many small task groups, not many demos of one task. iPhUMI makes this cheap because no robot time is consumed.

## Slide 12
STEP 8
Evaluate the frozen policy, not the video
BPP + iPhUMI on the Unitree G1 · step by step
12 / 15
8
Freeze the bundle, run the matrix, report paired differences.
Report | Required context
Completion and lift/hold (separately) | Denominator and 95% binomial interval; all initiated trials count
Prompt ablations | Correct / none / wrong-task / shuffled / retrieved, interleaved order
Prompt provenance | Prompt IDs, frame indices, similarity scores, context hash per trial
Latency | Capture → accepted target distribution, deadline misses
Learning cost | Demos, prompts, compute per method (BPP vs ICRT vs GR00T fine-tune)
Paired difference | Matched conditions, paired bootstrap interval
Go / no-go for ICL: correct prompts must produce the requested behaviour and beat the controls on held-out conditions with a paired interval excluding zero. A successful robot video is not evidence.
Notes: Independent verifier watches the cup, not the command. Fifty held-out conditions per method as a starting budget; the 95% interval at 50 trials is roughly ±14 points near 50%, so lean on paired, interleaved designs. Report counts of aborts, interventions and indeterminate outcomes.

## Slide 13
EVIDENCE
What the paper showed, and what it did not
BPP + iPhUMI on the Unitree G1 · step by step
13 / 15
Benchmark | Result | Takeaway
DrawAnything-Sim (2,000 train tasks, 50 unseen) | 80.7% error reduction vs goal-image; 33.3% vs ICRT | Dense step-by-step guidance from the prompt
DrawAnything-Real (ARX arm, iPhone wrist cam) | Reconstructs unseen drawings from one iPhUMI demo | iPhUMI prompts work at test time on hardware
LIBERO-Gen Combination / Chain | Beats language and goal-image; rivals π0.5 with no pretraining | Unseen combinations and chains of known primitives
Original LIBERO (4 suites) | 97.5 avg vs 96.2 language DP vs 97.2 π0.5 | No penalty on tasks language already describes
Laundry folding (3 tasks, low diversity) | BPP 76 / 100 / 60% vs language 96 / 100 / 100% | Weak conditioning when diversity is low
Not shown by the paper
• Any humanoid or Unitree G1 deployment
• A new action primitive from a single prompt (authors say no evidence yet)
• Prompts recorded in a substantially different environment from execution
Released artifacts (MIT)
• Training and deployment code, datasets and checkpoints for the benchmarks above
• iPhUMI hardware files and iOS app; real-env deployment submodule
• Related: Gated Memory Policy's in-the-wild iPhUMI cup-placement checkpoint
Notes: All numbers from arXiv:2606.30457. DrawAnything and LIBERO-Gen are the authors' own benchmarks. The laundry case study is the honest negative: with only three training tasks, language conditioning beat BPP because the prompt's extra spatial and temporal variation made task identification harder.

## Slide 14
TRANSFER TO THE G1
Risks, mitigations and the week-by-week checklist
BPP + iPhUMI on the Unitree G1 · step by step
14 / 15
Risk | Mitigation
Wrist-camera offset or gripper geometry differ from iPhUMI | Print the iPhUMI mount for the G1 gripper; overlay test at matched TCP poses before motion
Relative-EE action convention mismatched | Codec sign tests (identity, ±x, rotation signs, round trip) in the gateway before G4
Released checkpoint has no cup body-grasp in its training mix | Try Gated Memory Policy's cup checkpoint as a transfer sanity check; otherwise go to step 7
Low training diversity → weak prompt conditioning | Phase-2 diversity plan; scripted/sim variants; report the no-prompt control
Prompt from a different scene than execution | Start with matched layouts; add unmatched as a separate evaluation row
Week 1
Mount, calibrate, codec tests, iPhUMI width calibration
Week 2
Released checkpoint on our cup; shadow mode then G4 baseline
Weeks 3–4
Pilot data (120 demos), converter, first training run
Weeks 5–7
Diversity data, frozen bundle, two-cup pilot
Weeks 8–10
Held-out evaluation, paired report, go / no-go
Notes: Ordering follows the team deck: the pilot dataset validates the pipeline; the released checkpoint is tried before any training; ICRT is the fallback if the UMI-style action space cannot be reproduced on the G1 gripper.

## Slide 15
REFERENCES
Sources and companion material
BPP + iPhUMI on the Unitree G1 · step by step
15 / 15
Behavior Prompting Policy: Demonstrations as Prompts for Manipulation
Patel, Pekarek, Castro Hernandez, Song · arXiv:2606.30457 · 2026
real-stanford/behavior_prompting
Code, datasets, checkpoints, deployment (MIT)
real-stanford/iPhUMI
Handheld interface, iOS app, hardware files
Project page
behavior-prompting.github.io
Universal Manipulation Interface (UMI)
Chi et al. · RSS 2024 · the gripper and action convention BPP inherits
Diffusion Policy
Chi et al. · RSS 2023 · the action decoder
ICRT: In-Context Imitation Learning via Next-Token Prediction
Fu et al. · ICRA 2025 · the fallback route
Gated Memory Policy
Gao et al. · 2026 · in-the-wild iPhUMI cup-placement checkpoint
Team deck & engineering guide
G1_ICL_Team_Presentation · G1_Open_Source_ICL_Engineering_Guide
G1-specific values (rates, offsets, budgets, weeks) are proposals; no G1 hardware validation was performed for this deck.
Notes: Use the team deck and the engineering guide for the surrounding architecture, gates and statistics.