## Slide 1
TWO-PART DECK · 18 SEPTEMBER 2026
In-context learning for robots:
what should actually go in the context?
Part 1 · A taxonomy of robot context, after Siyin Wang's essay (Aug 2026)
Part 2 · MimicDroid, step by step: humanoid ICL from human play videos
The question worth caring about is not how many tokens are in the context. It is whether the context contains the specific information the policy is missing but the task requires.
Sources: sinwang20.github.io/blog/robot-icl-en · Shah et al., MimicDroid, arXiv:2509.09769 (ICRA 2026) · ut-austin-rpl.github.io/MimicDroid
Notes: Part 1 follows the structure of the essay: why context, three kinds of uncertainty, robot demos, human video, task-agnostic motion, pretraining-scale context, selection and state, open problems, cheat sheet. Part 2 is a mechanical walkthrough of MimicDroid with the paper's numbers.

## Slide 2
PART 1 · WHY CONTEXT
Why a policy needs context at all
Robot in-context learning: what goes in the context · MimicDroid step by step
02 / 23
The standard form and its bet
π(aₜ | oₜ, l): current observation plus a language instruction → next action.
Hidden assumption: the current frame is sufficient. History's role has been compressed into the weights.
Where the bet breaks at deployment
• Frame doesn't reveal how far into the task you are
• Camera moved: pixel motion ↔ robot coordinates changed
• Arm or end-effector swapped: same command, new kinematics
• Same task admits many styles: fast, slow, careful
• New objects, scenes, combinations
π( aₜ | oₜ , l , 𝒞 )
𝒞 is the context: a demonstration trajectory, a human video, a goal image, a few seconds of the robot's own poking around, or the execution history so far.
The n-gram lesson: "The keys to the cabinet ___ on the table" needs a word five tokens back. Every token you add to the context makes sparsity worse — unless you stop counting and start generalising. Which leaves exactly one question: what should go in 𝒞?
Notes: Almost every VLA is π(a_t | o_t, l): current frame + proprio + language. The clean form hides a Markov assumption: everything needed to pick the next action is in the current frame, with history compressed into the weights. Language modelling made the same bet with n-grams and it died of long-range dependency and data sparsity. Robotics is in the same place.

## Slide 3
PART 1 · THE TAXONOMY
Which uncertainty is the context resolving?
Robot in-context learning: what goes in the context · MimicDroid step by step
03 / 23
π(aₜ | oₜ, l, 𝒞) = f_θ(aₜ | oₜ, z), z = z(𝒞)
 | z is | z(𝒞) is | the context contains | examples
Selection | an index into existing mappings | a lookup | a description of z | language, goal image, URDF, episode metadata (π0.7)
State | the hidden state of this episode | filtering / retrieval | fragments of world state | last frames; MemoryVLA, MemER, MEM, HiMe
Learning | the mapping itself | induction | samples from f_z | demo trajectories, human video, random-motion triplets
Only the third one is learning. Selection and state are just as useful and just as context-dependent — but after the model finishes reading, the function it uses to turn observations into actions has not changed.
The LM origin
Three English→French pairs in the prompt; the model writes "fromage" for cheese. Acquired inside the window (in-context) and holds on unseen inputs (learning).
The robot analogue
Instruction = spec; demonstration = worked example of (observation, action) pairs from which the model infers what this task is, then does it in a new scene. Weights frozen.
Notes: Split the policy into the part frozen at training time and the part determined by context: π(a|o,l,C) = f_θ(a|o,z), z = z(C). The question is whether the context gives you the name of z or sample points on f_z. Only the third row is learning: after reading, the function that turns observations into actions has changed.

## Slide 4
PART 1 · LEARNING FROM ROBOT DEMOS
Teleop trajectories as context: three things must hold
Robot in-context learning: what goes in the context · MimicDroid step by step
04 / 23
1
The objective creates the ability
One-Shot IL (2017): many distinct tasks, each with one demo and one execution; optimise performance after reading the demo. The demo is a task condition, not a history buffer.
2
The form decides the difficulty
ICRT: interleave image/state/action tokens, next-token prediction, prepend 1–2 trajectories at test time. Instant Policy: demo, observation and future actions as graph nodes; diffusion over the graph. KAT: keypoints + action tokens read by a text Transformer. BPP: cross-attend a compressed demo embedding with the current observation. StellaVLA: task plans, subgoals and 3D motion in structured form.
3
Pairs have to come from somewhere
Recombine: one demo as prompt, others of the same task as queries (ICRT, BPP). Generate: procedural tasks in sim (One-Shot IL), pseudo-demos (Instant Policy), purely synthetic RGB (SynthICL). Bolt on: RICL retrieves snippets from 10–20 user demos into a post-trained π0-FAST.
Tokenization matters on the action side too: a tokenizer that reconstructs trajectories well may not preserve temporal smoothness (Action Tokenizer Matters → LipVQ-VAE; HiST-AT). Discontinuous action tokens turn good demo correspondences into jerky control.
Notes: The induction ability comes from the objective (One-Shot IL pairs a demo with an execution and optimises performance after reading the demo). The form the demo takes decides how hard induction is. And you need enough demo–query pairs.

## Slide 5
PART 1 · HUMAN VIDEO AS THE DEMO
Video has no action labels, and a human body is not a robot body
Robot in-context learning: what goes in the context · MimicDroid step by step
05 / 23
Vid2Robot · align directly
Human video + robot state → actions via cross-attention. Trained on video–trajectory pairs with a contrastive loss pulling human-video and robot-video representations together. Shows cross-object motion transfer.
MimicDroid · skip the pairing
Only continuous, unlabeled human play video. Mine trajectory pairs with similar behaviour; train to watch one and predict the other. Human video is both context and supervision; no robot data to form pairs. Wrist-pose retargeting + random patch masking close the gap.
Point Policy · shared representation
Human hand pose and object state → semantic keypoints. Humans and robots look different in pixels and similar in keypoint space, so the mapping is easier to induce. Robust to novel objects and distractors on 8 real tasks.
MimicDroid's question is not "how do we back-fill action labels onto video" but "which part of human behaviour is structurally reusable across embodiments". Part 2 of this deck walks it step by step.
Costs to remember: video shows how the hand moved, not how hard the gripper squeezed; hand-pose estimators fail when hands vanish behind furniture.
Notes: Teleop is expensive on both ends. Human video is cheap and abundant but carries no joint angles or grip force, and the mapping the model must induce has an embodiment gap running through it. Three ways across.

## Slide 6
PART 1 · SYSTEM, NOT TASK
Random motion is also a good demonstration (ICWM)
Robot in-context learning: what goes in the context · MimicDroid step by step
06 / 23
ICWM · In-Context World Modeling
Before the task, let the robot move randomly for a few seconds. Record (o_start, a, o_end) triplets and pack them into the context. They say nothing about where to go; they say what an action does to the image in this system.
Why it still counts as learning
After reading the triplets, the way the model turns observations into actions has changed — not a selection among mappings, not a state estimate. The object of induction switched from the task to the system.
Collection cost drops to nothing: no human, no labels, no task binding. One exploration segment serves every task at that workstation; bump the camera or swap the gripper and you re-run a few seconds.
For our G1: this is the cheapest recalibration primitive on the list, and it composes with any of the task-context methods.
Notes: Camera moved 20 cm; task, demo and image all look fine; action lands in the wrong place. The missing information is not the task but the system: under this camera and body, what does an action do to the image? Everything else assumes the system configuration is fixed.

## Slide 7
PART 1 · WHEN CONTEXT REACHES PRETRAINING SCALE
Two lessons from large models: shortcuts and emergence
Robot in-context learning: what goes in the context · MimicDroid step by step
07 / 23
Qwen-RobotManip · the context shortcut
If training always supplies the H chunks right before the current step, the model copies the last chunk's actions: low loss, useless context, collapse when recent history is atypical.
Fix: stochastic context sampling — sample the window from random positions in the episode so recency cannot be exploited; deploy with a rolling window. Remove it and you get very low training loss and very poor success.
GEN-1.5 · a one-shot ability nobody trained for
Physical prompt = 3–12 s of sensorimotor data in a 30 s window. 59% ± 10% one-shot across 10 tasks; 83% ± 9% after 10 gradient steps on 5 minutes. No ICL architecture, no auxiliary objective, prompts introduce time jumps never seen in training.
Derivatives: composed prompts, sim-recorded prompts, human hands in view, 1-step adaptation at 66.5%.
Same category as human video (sensorimotor pairs → task mapping), with one difference: the source of the context does not have to share an embodiment with the executor.
Notes: Qwen-RobotManip conditions on recent (o, s, a) triplets from the same episode to adapt behavioural style with no parameter updates, and reports the context shortcut. GEN-1.5 is the only reported case of ICL appearing without being trained for.

## Slide 8
PART 1 · THE OTHER TWO USES OF A WINDOW
Selection, state, and the orthogonal road of test-time training
Robot in-context learning: what goes in the context · MimicDroid step by step
08 / 23
Use | What it resolves | Representative work | Does f change?
Selection | Which existing mapping to run; style, speed, grasp choice | π0.7 (language + subtask + metadata + subgoal images) | No — metadata picks one
State / memory | Where did I put the cup; which stage am I on | MemoryVLA, MemER, ContextVLA, MEM (15-min tasks), HiMe (Executor / Sentry / Planner) | No — the state fed to f changes
Selection & compression | Which frames to keep; spurious long-sequence correlations | Big Picture Policies (VLM picks keyframes), Gated Memory Policy (learns when to read) | No
Test-time training | Same deployment evidence, written into weights | RoboTTT (8K steps into fast weights), VANE (commit updates only if visual outcomes support them) | θ changes, not z
Execution history written out — (o₁,a₁),(o₂,a₂),… — is formally identical to a demonstration. The difference is what changes after you read it.
Test-time training overlaps ICL in goals but not costs: it needs gradients, is hard to roll back, and adds online safety requirements.
Notes: π0.7 packs language, next subtask, episode metadata and subgoal images into one prompt — a powerful control interface, but the mappings already exist in the weights. Memory methods solve partial observability inside a task. Test-time training writes the same evidence into weights instead.

## Slide 9
PART 1 · WHAT IS STILL OPEN
Three open problems the essay leaves us with
Robot in-context learning: what goes in the context · MimicDroid step by step
09 / 23
1 · How does ICL emerge?
LLM ICL was not trained; it appeared from next-token prediction. Robotics runs the other way — almost everything trains the ability explicitly. GEN-1.5 is the only reported emergent case, mechanism unstudied.
What data distributions produce it? Does explicitly trained ICL generalise differently from emergent ICL?
2 · What form does a demo take?
Interleaved tokens, graph nodes, keypoints, chunk embeddings, structured plans, interaction triplets, raw sensorimotor sequences — almost never compared head to head.
High abstraction eases induction but discards contact, force and material; low abstraction keeps everything and makes the model find correspondence itself.
3 · How do we scale context?
A VLA must emit actions at a high rate; every token adds cost to every decision. Which information must be kept frame by frame, which can be squeezed into a token, which can be dropped?
MimicDroid hits this directly: gains plateau beyond 3 in-context examples because of training-time context length.
Conclusion of the essay: robot ICL is moving past transplanting the GPT prompt analogy. What it changes is what the policy looks at — and whether that contains the information the task requires.
Notes: Emergence, representation, and context scaling. The third is not the LLM long-context problem: there the cost is latency; here the control loop may stop closing.

## Slide 10
PART 1 · CHEAT SHEET
What goes in, what gets induced, at what budget
Robot in-context learning: what goes in the context · MimicDroid step by step
10 / 23
Method | What goes in the context | What gets induced | Adaptation budget
One-Shot IL | one robot demo | task rule | 1 demo
ICRT | 1–2 teleop trajectories | task rule | 1–2 demos
RICL | snippets retrieved from 10–20 demos | task rule | 10–20 demos
Instant Policy | demo + current obs (as a graph) | task and local correspondence | 1–2 demos
BPP | one handheld-collected demo | new behaviour | 1 demo
KAT | keypoints + action tokens | vision–action correspondence | ~10 demos
Vid2Robot | human manipulation video | motion intent | 1 video
MimicDroid | unlabeled human play video | cross-embodiment reusable behaviour structure | 1–3 clips
Point Policy | human video → semantic keypoints | morphology-agnostic intent | offline video
ICWM | task-agnostic random interaction triplets | this system's observation–action mapping | a few seconds of motion
GEN-1.5 | 3–12 s human demonstration | task rule | 3–12 seconds
Qwen-RobotManip | within-episode execution history | current embodiment identity / style | within-episode
Notes: Reproduced from the essay's cheat sheet with light edits.

## Slide 11
PART 2
MimicDroid, step by step
In-context learning for humanoid manipulation from human play videos
Shah, Liu, Wang, Jiang, Kumar, Seo, Martín-Martín, Zhu · UT Austin · ICRA 2026
1
Collect play videos
2
Extract actions from hands
3
Mine context–target pairs
4
Bridge the embodiment gap
5
Meta-train for ICL
6
Prompt the humanoid with 1–3 videos
Notes: Correction to note for the team: MimicDroid's real-world humanoid is the Fourier GR1, not a Unitree G1. The method is embodiment-agnostic in task space (wrist pose + IK), so a G1 port is a retargeting exercise, but no G1 result or checkpoint exists.

## Slide 12
PART 2 · OVERVIEW
What MimicDroid is, in one picture
Robot in-context learning: what goes in the context · MimicDroid step by step
12 / 23
Play videos
10-min sessions, one static RGB camera
Hand poses
WiLoR → wrist 6-DoF + grasp
Similar pairs
DINOv2 + actions, cosine top-k
Meta-ICL policy
long-context transformer, L1 on 32-step chunks
Humanoid
retarget wrist → IK → execute
The setup
Test: D_test = {τᵢ^demo}, 1–3 human RGB videos of task 𝒯. Train: D_train = human play trajectories only; an implicit task distribution induced by natural play. Policy π_θ must use the demos in context, no parameter updates.
The two challenges
(a) Construct training samples: play video has RGB only — actions, proprio and context–target pairs must be manufactured.
(b) Cross the embodiment gap: kinematic (human hand → humanoid wrist) and visual (human appearance and occlusion).
The claim
Trained on play videos alone, the policy adapts in-context to novel objects and environments; nearly 2× the real-world success of the video-conditioned baseline and +26% over test-time fine-tuning, instantly.
Meta-ICL objective: 𝔼_𝒯 𝔼_{σᶜᵗˣ, σᵗᵍᵗ} [ ℒ_𝒯( π_θ(σᵗᵍᵗ | σᶜᵗˣ) ) ] — context trajectories show how; the target trajectory supervises.
Notes: Problem: at test time the robot gets 1–3 RGB videos of a human doing a novel task and must perform it under different object placements, weights frozen. Training data: only human play videos, 10–20 minutes per session, curiosity-driven, ~18× faster to collect than teleop and inherently diverse.

## Slide 13
PART 2 · STEP 1
Collect human play videos — no robot, no labels, no task resets
Robot in-context learning: what goes in the context · MimicDroid step by step
13 / 23
1
Point one static RGB camera at a workspace and let a person play for ten minutes.
 | Real world | Simulation (benchmark)
Interaction | Operator's own single hand | Two free-floating 6-DoF hands via space mouse
Session length | ~10 minutes | 20 minutes
Cameras | One static RGB camera | Three cameras to cover the workspace
Total collected | 45 min · 80k frames (1 h in appendix) | 8 h · 320k timesteps · 30 objects · 8 kitchens
Layout | Randomised kitchen and object layouts per session | RoboCasa scenes, randomised
Output of step 1: raw trajectories τ = {sₜ}, RGB frames only. Compared with teleop, play data is about 18× faster to collect and naturally contains recurring behaviours ("bread to oven" … "bagel to oven") that step 3 will mine.
Real evaluation and play data in the paper use the Fourier GR1 humanoid. For a Unitree G1 the videos are the same; only the retargeting target changes (step 4).
Notes: An operator interacts freely with the scene, driven by curiosity: open the oven, put bread on the tray, later move it elsewhere. Play captures more diversity of interactions and object configurations than goal-directed teleop because there are no task goals and no task-specific resets.

## Slide 14
PART 2 · STEP 2
Extract actions and proprioception from the hands
Robot in-context learning: what goes in the context · MimicDroid step by step
14 / 23
2
Run a hand-pose model on every frame; the next pose becomes this frame's action.
for each frame s_t in a play video:
h_t = WiLoR(s_t) # wrist 6-DoF (camera frame) + grasp from finger angles
a_t = h_{t+k} # intended action = future hand pose (real world: k = 1)
s'_t = { s_t, h_t } # observation = object-centric RGB crop + proprio (hand pose)
processed trajectory: τ' = { (s'_t, a_t) }_{t=1..T}
action chunking: predict l = 32 future actions per step
Why this works on a humanoid
Operating in task space (Cartesian wrist pose) and exploiting kinematic similarity between humans and humanoids preserves task intent without asking demonstrators to move like a robot (cf. OKAMI, Humanoid Policy ~ Human Policy).
Output of step 2: state–action trajectories with the same form as robot data — except every action came from a person's hand.
Known failure: the estimator handles partial occlusion with hand priors, but fails when hands vanish (reaching into cupboards, behind furniture). The authors suggest adding full-body motion estimation.
Notes: Video has no action labels, so the future hand pose is treated as the action. An off-the-shelf hand pose estimator (WiLoR) predicts the wrist pose and a grasp signal from finger joint angles, per frame. Real world: k = 1, 6-DoF wrist pose w.r.t. the workspace camera plus a binary gripper. The current hand pose is also fed as proprioception.

## Slide 15
PART 2 · STEP 3
Mine context–target pairs from continuous play
Robot in-context learning: what goes in the context · MimicDroid step by step
15 / 23
3
Let recurring behaviour in play data define the task groups — no labels needed.
φ(σ) = [ (1/T) Σ_t DINOv2(s_t) , a_1, …, a_T ] # visual summary + action sequence
for each sampled target segment σ_tgt ⊂ τ':
score(σ) = cos( φ(σ_tgt), φ(σ) ) for every other segment σ in the dataset
context = top-k by score # k = 50 retrieval pool; 3 used per training sample
sample = ( {σ_ctx_i}, σ_tgt )
What a pair looks like
Target: "move bread from plate to oven". Retrieved context: "move bagel from plate to oven", "move cup from counter to tray" — different objects, same observation–action pattern.
Choice | Effect reported
Small k | Limits training diversity
Large k | Includes dissimilar segments; performance drops from noise
k = 50 | Balance between diversity and noise (their setting)
Mean-pooled DINOv2 + actions | Robust to background clutter; captures the observation–action distribution rather than pixels
Notes: Meta-ICL needs (context, target) pairs from the same task, but play videos have no task labels. MimicDroid samples a target segment, embeds it, and retrieves the top-k most similar segments across the dataset as context. Similarity is cosine over [mean-pooled DINOv2 frame features, a₁ … a_T]. k = 50 as the retrieval pool balances diversity against noise; each training sample uses 3 context trajectories + 1 target.

## Slide 16
PART 2 · STEP 4
Bridge the embodiment gap: kinematic and visual
Robot in-context learning: what goes in the context · MimicDroid step by step
16 / 23
4
Retarget in task space; mask patches so the policy stops looking at the human.
Kinematic gap → wrist retargeting
human wrist pose (camera frame)
→ humanoid wrist pose (robot base frame)
→ inverse kinematics → arm joint angles
Task space preserves intent; the demonstrator never has to mimic robot morphology. Grasp signal → hand open/close.
Visual gap → random patch masking
During training, with probability p = 0.8, mask a uniformly sampled 1–16 patches of the input image.
Ablation (sim, averaged L1–L3): abstract→humanoid drop is −17% without masking, −3% with it. Real world: 0.53 vs EgoMimic-style hand masking 0.58, with no SAM segmentation needed.
For a Unitree G1 | What changes
Retarget target | GR1 wrist frame → G1 wrist frame; G1 arm IK with joint/velocity limits and torso/head collision model
Hand | Binary grasp → parallel gripper width or Dex3 synergy; calibrate once
Camera | Static workspace camera pose must be known w.r.t. the G1 base; hand poses were estimated in the camera frame
Notes: Kinematic: predicted human wrist poses are retargeted to humanoid wrist poses and inverse kinematics gives joint angles. Visual: random patch masking during training, applied with probability p = 0.8, masking 1–16 patches, so the policy stops relying on human-specific appearance. Removing masking costs 17 points on transfer to the humanoid versus 3 with it.

## Slide 17
PART 2 · STEP 5
Meta-train the policy to learn in context
Robot in-context learning: what goes in the context · MimicDroid step by step
17 / 23
5
Each gradient step: watch three similar clips, predict the fourth.
L_BC = Σ_t || π( a_{t:t+32} | s'_{1:t}, a_{1:t-1}, {σ_ctx_i}_{i=1..3} ) − a_{t:t+32} ||_1
training sample = 3 context segments + 1 target segment
segment length = 256 steps (sim) / 128 steps (real), inputs downsampled ×4
tokens per step = observation + action tokens; 32-action chunk out per step
masking = p = 0.8, 1–16 patches (step 4)
Why chunking
Play data is multimodal; predicting 32 future actions per step (ACT-style) models that better than next-action prediction and keeps the output rate high while inputs are downsampled.
Scaling result (sim) | 128k frames | 320k frames
L1 · seen objects, seen env | 35% | 59%
L2 · unseen objects, seen env | 21% | 45%
L3 · unseen objects, unseen env | 16% | 27%
Consistent gains at every level as play data grows — the argument that this data source scales.
Notes: Behaviour cloning with the Meta-ICL objective: each instance = 3 context segments + 1 target; predict 32-step action chunks for the target with an L1 loss, conditioned on its past observations/actions and the context. Backbone: long-context transformer with modality-specific encoders. Segments are 256 steps in sim and 128 in the real world, inputs downsampled ×4 for cost, output rate unchanged.

## Slide 18
PART 2 · STEP 6
Test time: show the humanoid one to three human videos
Robot in-context learning: what goes in the context · MimicDroid step by step
18 / 23
6
Film a person, hand the clips to the frozen policy, let the humanoid go.
Record
1–3 human videos of the novel task, same static camera
Process
WiLoR poses → (s', a) sequences, as in step 2
Context
Place the processed clips in the transformer context
Predict
32-step chunk of humanoid wrist poses + grasp, conditioned on own history + context
Execute
Retarget → IK → joint targets; re-observe; repeat
INPUT = { human video 1..3 as (s', a) } + robot's own s'_{1:t}, a_{1:t-1}
OUTPUT = a_{t:t+32} → humanoid wrist pose + grasp per step → IK → joints
Swap the videos, keep the weights: a different task on the same scene. This is the same two-cup test we use for BPP — only the prompt modality (video of a person) differs.
Context-count result: +gain from 1→3 examples, diminishing at 4–6; extending context length scales memory and compute linearly.
Notes: The policy receives 1–3 human RGB videos of the new task, possibly with novel objects and environments, processes them exactly as in step 2, places them in context, and predicts action chunks conditioned on its own past observations and the context. No parameter updates. Performance improves from 1 to 3 examples and plateaus at 4–6 because of training-time context length.

## Slide 19
PART 2 · RESULTS
What the paper measured
Robot in-context learning: what goes in the context · MimicDroid step by step
19 / 23
Method | Abstract L1 | L2 | L3 | GR1 L1 | L2 | L3
H2R (goal image) | 0.03 | 0.05 | 0.03 | 0.03 | 0.00 | 0.00
Vid2Robot (video) | 0.44 | 0.40 | 0.12 | 0.41 | 0.23 | 0.11
PEFT (fine-tune at test) | 0.47 | 0.35 | 0.00 | 0.29 | 0.21 | 0.01
MimicDroid w/o masking | 0.59 | 0.51 | 0.22 | 0.37 | 0.35 | 0.09
MimicDroid | 0.73 | 0.39 | 0.27 | 0.59 | 0.44 | 0.26
Real world · GR1
MimicDroid 0.53 / 0.23 / 0.08 (L1 / L2 / L3) vs Vid2Robot 0.28 / 0.08 / 0.00 — nearly twofold. Tasks: pick-and-place to receptacles, opening and closing an oven tray; seen objects (chips, bread, apples) and unseen (potatoes, garlic, cloth).
Versus fine-tuning
+29% (abstract) and +26% (humanoid) over PEFT, and instant. PEFT fails at L3 (forgetting under large shift) and overfits the source embodiment: −10% abstract→humanoid vs −3% for ICL.
Failure analysis
Task misidentification 26%, missed grasps 16%, other 8% (incomplete closure, missed placement). ICL cuts misidentification by 15 points vs Vid2Robot. L3 still hard: novel motions (a bottom-to-top faucet) and overfitting to one operator's hand size.
Notes: Baselines trained on the same play videos with identical augmentation: H2R (goal-image), Vid2Robot (video-conditioned, no actions in context), PEFT (test-time fine-tuning). Sim numbers are success rates on the authors' RoboCasa-based benchmark; real numbers are on the GR1.

## Slide 20
PART 2 · LIMITS AND OUR USE
Limitations the authors state, and what a G1 port would need
Robot in-context learning: what goes in the context · MimicDroid step by step
20 / 23
Item | Status | Implication for us
Released artifacts | Benchmark code and dataset (RoboCasa-based); no policy checkpoint verified | A training project, not a download
Real-world embodiment | Fourier GR1, not Unitree G1 | Retargeting target and IK change; the pipeline does not
Prompt modality | Plain RGB video of a person, 1–3 clips | Cheapest possible demonstration; fits phase 3 of the plan
Data needed | 45 min real play gave the reported GR1 results; scales with more | Film several operators to avoid hand-size overfitting
Context budget | Gains plateau beyond 3 clips | Do not plan on many-shot prompting
Contact / force | Not modelled; grasp is a binary signal from finger angles | Pair with a NEXT-style external-torque verifier on the G1
Reading the essay's taxonomy back onto MimicDroid: its context carries samples of the mapping (row 3, learning), sourced from a different embodiment, with the pairing manufactured by similarity instead of labels. That is why it belongs with GEN-1.5 and S1 conceptually — and why it is the only open one of the three.
Notes: Three stated limitations: reliance on curated play video (web video is the extension), hand-pose failure when hands vanish, and treating demos as low-level state–action sequences — it learns how, not why, so it cannot generalise across semantically equivalent tasks; language–trajectory meta-training is the suggested fix.

## Slide 21
PART 2 · COMPARISON
MimicDroid next to the other demo-in-context methods
Robot in-context learning: what goes in the context · MimicDroid step by step
21 / 23
 | MimicDroid | BPP + iPhUMI | ICRT | GEN-1.5 / S1
Context | 1–3 human RGB videos | One handheld sensorimotor demo | 1–2 teleop trajectories | 3–12 s sensorimotor clip / one video
Training data | Human play video only | Diverse handheld demos, many tasks | Teleop demos, multi-task | Large proprietary engines
Pairing | Mined by similarity, no labels | Same task group | Same task | Emergent / undisclosed
Embodiment gap | Wrist retargeting + patch masking | Matched wrist camera + gripper | Same robot | Handled in-model
Weights | Not released | Released (MIT) | Released (Franka) | Closed
Where it fits for us | Phase 3 training target | First frozen-weight candidate | Fallback if BPP won't map | Concept and upper bound
Same acceptance test for all: change only the prompt, hold weights and scene fixed, and the behaviour must follow the prompt on held-out conditions.
Notes: Use this with the team deck's Act 2: BPP is the first frozen-weight candidate because it ships checkpoints; MimicDroid is the humanoid-native end state because its prompt is a plain video and it needs no robot data to train.

## Slide 22
REFERENCES
Sources
Robot in-context learning: what goes in the context · MimicDroid step by step
22 / 23
In-Context Learning for Robots: What Should Actually Go in the Context?
Siyin Wang · blog · Aug 22, 2026
MimicDroid: In-Context Learning for Humanoid Robot Manipulation from Human Play Videos
Shah et al. · ICRA 2026 · arXiv:2509.09769
MimicDroid project page and benchmark
ut-austin-rpl.github.io/MimicDroid · UT-Austin-RPL/mimicdroid-robocasa
One-Shot Imitation Learning
Duan et al. · NeurIPS 2017
ICRT
Fu et al. · ICRA 2025
Instant Policy
Vosylius & Johns · ICLR 2025
Behavior Prompting Policy
Patel et al. · 2026
RICL
Sridhar et al. · CoRL 2025
Vid2Robot
Jain et al. · RSS 2024
Point Policy
2025
In-Context World Modeling for Robotic Control (ICWM)
2026
Qwen-RobotManip Technical Report
2026
GEN-1.5
Generalist AI · Aug 2026
π0.7
Physical Intelligence · 2026
RoboTTT · VANE · MEM · HiMe · Gated Memory Policy
2026 memory and test-time-training references

## Slide 23
CLOSING
Three takeaways
Robot in-context learning: what goes in the context · MimicDroid step by step
23 / 23
Ask what is missing
Context is worth adding only when it carries the specific information the current frame lacks and the task requires: the mapping (learning), the episode state, or which existing mapping to run (selection). Name which one before choosing a method.
Video can be the demo
MimicDroid shows the full pipeline from a person's play video to a humanoid's wrist trajectory with no robot data: hand poses as actions, similarity-mined pairs as tasks, retargeting plus masking as the bridge. Nearly 2× real-world success over video conditioning; +26% over test-time fine-tuning.
Know the boundaries
No released MimicDroid weights; real results are on a GR1; gains plateau beyond 3 clips; contact is a binary grasp. For our G1: film play data now, train later, and keep BPP as the first frozen-weight route while this one is built.
Next step on our side: a 10-minute play-video pilot with the cup task on our bench, processed through WiLoR, to confirm hand-pose quality before committing training compute.