## Slide 1
SYSTEM DESIGN / IMPLEMENTATION BLUEPRINT
FROM INSTRUCTION
TO GROUNDED ACTION
Unitree G1 • Active perception • Semantic memory
Nav2 navigation • GR00T VLA pick & place
2 COMPLETE WORKED TASKS
OFFLINE-FIRST
LANGUAGE
ACTIVE PERCEPTION
SEMANTIC WORLD
NAVIGATION
VLA MANIPULATION
DETAILED TECHNICAL DECK • OCT 2026
Notes: This is a proposed architecture and implementation design, not evidence of verified real-G1 task success. Focus on separating semantic task planning, active perception, navigation goals, and VLA pick/place execution. Two examples are studied: move a red cup to a kitchen counter; dispose of a user-authorized disposable cup in a trash bin.

## Slide 2
G1 / EMBODIED SYSTEMS
MOTIVATION
The difficult part happens before grasping
A camera can detect a cup only after the robot observes the right place.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
02
“Find the red cup on the living-room table, pick it up, and place it on the kitchen counter.”
WHAT?
Identify the correct object, attributes, support surface, and destination.
WHERE?
Use world memory or actively select viewpoints to search the scene.
HOW?
Use separate navigation, VLA pick, navigation, and VLA place skills.
Notes: A raw detector does not translate an instruction into where to look. The high-level planner must issue a grounded search specification; a separate active perception agent resolves that specification using memory, viewpoints, and the existing 3D detector. Only after the object is grounded may the task planner request navigation and manipulation.

## Slide 3
G1 / EMBODIED SYSTEMS
SCOPE
Two tasks, one reusable execution contract
Same world model and skill interfaces; different destinations and task policies.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
03
CASE A / DELIVERY
Red cup → kitchen counter
Pick is separate from walking; place is separate from arrival.
CASE B / TABLE CLEANUP
Disposable cup → trash bin
Disposal is permitted only after policy/intent verification.
Notes: The architecture must not implicitly throw away reusable household property just because the task says clean the table. In the second case the target is a disposable cup explicitly designated for trash, or confirmed by an authorized user/approved disposal policy. The same seven-stage execution chain is reused.

## Slide 4
G1 / EMBODIED SYSTEMS
SEPARATION OF CONCERNS
Who owns each decision?
Avoid asking one VLM to simultaneously reason, search, walk, grasp, and verify.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
04
01
MISSION PLANNER
What goal?
Which object?
What next?
02
ACTIVE PERCEPTION
Where to look?
Which viewpoint?
Is target visible?
03
SEMANTIC WORLD
Which ID?
Where observed?
What relations?
04
NAVIGATION
Where to stand?
Which route?
Did we arrive?
05
VLA MANIPULATION
How to pick?
How to place?
Did action succeed?
Independent safety supervisor gates every motion command and can stop execution regardless of planner output.
Notes: High-level planner typically uses RynnBrain-Plan-8B or a deterministic BT. Active perception can be a deterministic state machine. Semantic world is a separate persistent service. Navigation uses Nav2-style geometric planning plus a G1-compatible locomotion adapter. VLA manipulation uses a task-trained GR00T N1.7 policy with compatible embodiment. Safety is independent and cannot be bypassed by the VLM.

## Slide 5
G1 / EMBODIED SYSTEMS
SYSTEM ARCHITECTURE
One shared world, three agent loops
The memory layer connects instruction understanding to physically grounded actions.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
05
USER / MISSION
Natural-language task
HIGH-LEVEL PLANNER
Decompose / select next skill
SKILL ORCHESTRATOR
Validate, dispatch, monitor
SEMANTIC WORLD MODEL
SQLite object registry + 3D graph
ACTIVE PERCEPTION
Memory → viewpoint → observe
NAVIGATION
Goal pose → Nav2 → G1 walk
VLA MANIPULATION
GR00T pick / place + verify
G1 CONTROLLERS + SAFETY
Walking, arms, hands, E-stop
PERCEPTION INPUT: costmap • 3D detector • scene mesh • TF2
Notes: The architecture intentionally separates three loops: (1) mission planning chooses the next semantic skill, (2) active perception searches for ungrounded objects, and (3) skill execution and verification update the world model. Shared world receives 3D detections, costmap, reconstruction references and robot localization, though costmap remains geometrically authoritative in navigation. Nav2 does not directly control G1 balance; the locomotion interface must be validated.

## Slide 6
G1 / EMBODIED SYSTEMS
EXECUTION CONTRACT
Seven steps — four distinct motion skills
There is no combined “navigate + pick” or “navigate + place” operation.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
06
01
PARSE
Mission → typed goals
02
FIND
Active perception
03
NAVIGATE
To pickup pose
04
VLA PICK
Grasp & verify
05
NAVIGATE
To destination
06
VLA PLACE
Release & verify
07
CLOSE
Update world model
GATE: start each next skill only after the previous skill returns a verified terminal result.
Notes: This sequence is the core change requested. Stage 3 navigation ends at an approach pose with confirmed arrival; Stage 4 is independently invoked VLA pick. Stage 5 navigation transports the verified object while attached, Stage 6 is a separately invoked VLA place. Do not equate action goal acceptance with physical task completion. Observe→act→verify occurs at every stage.

## Slide 7
G1 / EMBODIED SYSTEMS
PHASE 0 / INSTRUCTION UNDERSTANDING
Parse language into typed mission constraints
The VLM specifies the target and destination; it does not invent object coordinates.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
07
CASE A: MOVE CUP
target: cup
color: red
room: living_room
support: table_03
destination: kitchen_counter
CASE B: CLEAN TABLE
goal: clear_table
target: disposable_cup
support: table_03
destination: trash_bin_01
disposal_authorized: true
Output is a validated mission specification, not a physical motion command.
Notes: The structured mission should include target attributes, room/surface relation, explicit destination, permitted skills and task policies. Case A move cup to kitchen counter; Case B clear table by disposing of a specifically user-authorized disposable cup. Validate schema and semantic constraints before running any action.

## Slide 8
G1 / EMBODIED SYSTEMS
PHASE 1 / SEMANTIC MEMORY
Query the world before moving the robot
Three outcomes determine whether to reuse memory, reobserve, or search from scratch.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
08
FIND OBJECT
class=cup, color=red, on=table_03
REGISTRY LOOKUP
positions + confidence + timestamps
Pose trustworthy?
FRESH & CONFIRMED
Reobserve quickly; proceed if matching.
STALE / UNCERTAIN
Visit expected location, verify again.
NO MATCH
Start Active Perception search.
“Not in memory” means “not yet observed” — never infer “absent” from a missing record.
Notes: The semantic registry should track last_seen, pose covariance, source, observation count, association probability and object lifecycle. Fresh+confirmed still needs near-task verification. Stale triggers verification at known location, no match triggers search. The semantics of NOT_FOUND vs NOT_OBSERVED should be explicit.

## Slide 9
G1 / EMBODIED SYSTEMS
PHASE 2 / ACTIVE PERCEPTION
A bounded search, not an unlimited wander
The agent chooses where to look, requests navigation, observes, and either grounds the target or stops.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
09
RESOLVE REGION
room + support table
PLAN VIEWPOINTS
coverage + reachability
NAVIGATE TO VIEW
safe G1 pose
OBSERVE
RGB + detector + TF2
MATCH?
YES → FOUND(object_id, evidence)
NO → NEXT VIEWPOINT / REOBSERVE
Search budget = max viewpoints • max time • max distance • perception confidence • operator stop
Notes: Implement ActivePerception as a ROS 2 action: goal target query, budget and authorized search region; feedback current viewpoint, coverage, candidate IDs, reason; terminal results FOUND / NOT_OBSERVED / UNSAFE / TIMEOUT / CANCELED. Search uses memory before motion. A viewpoint is an observation pose, different from a manipulation approach pose. Robots never move to unvalidated waypoints.

## Slide 10
G1 / EMBODIED SYSTEMS
PHASE 2 / VISUAL SEARCH
Plan observation viewpoints using the 3D scene
A good view exposes the tabletop without making the robot stand somewhere unsafe.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
10
TABLE
V1
V2
V3
VIEWPOINT SCORE
Q(view) =
1
Visibility
Can the camera see the support?
2
Coverage
Is this a new angle?
3
Path cost
Can G1 reach the viewpoint?
4
Safety
Is whole-body clearance valid?
Notes: The illustrative 2D map stands for a 3D geometry-aware viewpoint planner. Candidate points around table are sampled in traversable free space; FOV and visibility estimated by raycasting or coverage; cost from Nav2; safety from torso and limb clearance. Reject camera viewpoints in inaccessible or unstable areas. Choose in order of expected information gain balanced with travel and risk, then stop after the budget.

## Slide 11
G1 / EMBODIED SYSTEMS
PHASE 3 / GROUNDING
A detection is not yet the requested object
Class, color, support relation, map-frame pose, and confidence must agree.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
11
OBSERVATIONS
RGB / depth / 3D detector
EVIDENCE FUSION
class == cup
attribute.color == red
supported_by(table_03)
transform to map frame
pose & freshness valid
GROUNDED RESULT
object_id: cup_17
class: cup
color: red
pose: [2.4, 1.7, 0.82]
support: table_03
state: CONFIRMED
If RGB/3D attributes are insufficient → request another view; do not guess identity.
Notes: Input may be vision_msgs/Detection3DArray from an existing 3D detector with synchronized image. The detector may not supply color; add an RGB crop classifier or projected point colors. Use 3D support geometry to test on_top_of(table_03) with tolerances; do not conflate proximity with support. Ground an object only if constraints and confidence pass.

## Slide 12
G1 / EMBODIED SYSTEMS
SHARED WORLD / PERSISTENCE
A lightweight registry, not another SLAM pipeline
Persist identity and relations; reference heavy geometry in the existing reconstruction service.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
12
OBJECT RECORD
id: cup_17
label: cup; color: red
pose_map: (2.4, 1.7, 0.82)
pose_covariance: [...]
state: AVAILABLE
last_seen: 2026-10-29T...
geometry_ref: scene://cup_17
tracking_confidence: 0.94
SEMANTIC GRAPH
cup_17
red cup
table_03
living-room table
living_room
room region
ON_TOP_OF
IN_ROOM
SQLite object + observation + event + relationship tables; keep meshes/voxels in their source system.
Notes: Object registry can initially be SQLite with objects, observations, relations and events; schema needs stable IDs, pose uncertainty, last_seen, deleted/stale flags, transform source, and event version. Do not duplicate full mesh. Store geometry_ref and map_version, let geometric service resolve voxels or mesh. Optional Spark-DSG scene graph later.

## Slide 13
G1 / EMBODIED SYSTEMS
SHARED WORLD / LIFECYCLE
One cup ID across grasp, transport, and placement
Commands do not change object reality; verified events do.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
13
AVAILABLE
On table
RESERVED
Target locked
ATTACHED
Held by G1
PLACE PENDING
Released; verify
AVAILABLE
On destination
Verified grasp → attach cup_17 to G1 hand TF | Verified placement → detach and update cup_17 pose
Failure paths: grasp miss ⇒ AVAILABLE/UNCERTAIN • cup dropped ⇒ LOST + active re-localization • unverified release ⇒ PENDING
Notes: Object ID must not change when cup relocates. New observations are gated by lifecycle and tracking: ATTACHED is derived from hand-to-object transform and not re-associated as a new scene object. After VLA place reports release, set PLACE_PENDING, then verify cup in destination. The original Semantic-nav-amr only label+distance merges and cannot handle mobile object lifecycle robustly.

## Slide 14
G1 / EMBODIED SYSTEMS
BEFORE NAVIGATION / APPROACH
Pick-up viewpoint ≠ manipulation approach pose
A camera can see a cup from a place where the arms cannot reach it.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
14
TABLE
A
B
C
WALL
CANDIDATE RANKING
A ACCEPT
Free path + arm reachable
B REJECT
Body collision / obstacle
C REVIEW
Reachability margin low
Check traversability + clearance + IK
Notes: There are two distinct geometric problems: view selection for observing an object, and manipulation base pose selection for safely reaching it. Use arm IK/manipulability and contact feasibility, 3D body clearance, no-go zones, costmap path, balance and standing orientation. The approach goal is a candidate PoseStamped that can be validated and passed to Nav2; never simply use the detected object center or a fixed 0.7m offset.

## Slide 15
G1 / EMBODIED SYSTEMS
SKILL 03 / NAVIGATION
Navigate to the cup — no manipulation yet
Output: G1 is at a validated pickup pose and has stopped walking.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
15
FIND
NAVIGATE
VLA PICK
NAVIGATE
VLA PLACE
VERIFY
NAVIGATION REQUEST
goal: pose_A
frame_id: map
target_object: cup_17
mode: normal_walk
require_body_clearance: true
verify_arrival: true
NAVIGATION EXECUTOR
NAV2
Costmap route
G1 BRIDGE
Walk controller
RESULT
Arrived?
Gate: navigation SUCCEEDED + pose tolerance + stable stop.
Nav2 accepted a goal ≠ G1 arrived. Wait for the terminal result and independently verify the robot pose.
Notes: Nav2 NavigateToPose emits goal accepted, feedback and final result. ROS2 action semantics distinguish goal acceptance from physical completion. A separate G1 locomotion bridge must transform Nav2 path/pose commands into validated whole-body locomotion and ensure balance. Nav2 is NOT automatically a G1 balance controller. The handoff to VLA happens only after locomotion reports a stable terminal state.

## Slide 16
G1 / EMBODIED SYSTEMS
SKILL 04 / VLA MANIPULATION
VLA PICK — a separate skill from navigation
Input: close-range observation and grounded object ID; output: verified grasp or failure.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
16
FIND
NAVIGATE
VLA PICK
NAVIGATE
VLA PLACE
VERIFY
INPUTS
Object: cup_17
Instruction: pick red cup
RGB / hand state / proprioception
Validated pickup pose
GR00T N1.7 + G1 ADAPTER
Task-trained policy → action chunks
SONIC / hand controller, if supported
VERIFIED OUTPUT
Grasp state / object in hand
Tracking update: ATTACHED
Failure → reobserve or replan
Important: G1 embodiment support and pick-skill success require a compatible fine-tuned N1.7 policy.
Notes: GR00T N1.7 G1 SONIC interface is documented as a post-training embodiment; you need compatible fine-tuned checkpoint, task demonstrations and tested observation / action mappings. Do not treat unadapted base checkpoint as guaranteed pick skill. VLA command is pick(cup_17), not navigation. Verify grasp using camera/hand sensors and target motion, with timeout. Only then transition object to ATTACHED.

## Slide 17
G1 / EMBODIED SYSTEMS
SKILL 05 / NAVIGATION
Navigate to the destination while carrying
Carrying changes allowed motion and geometry; the cup moves with the robot, not with the old table.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
17
FIND
NAVIGATE
VLA PICK
NAVIGATE
VLA PLACE
VERIFY
LIVING
KITCHEN
BLOCK
CARRYING CONSTRAINTS
object_id remains cup_17
held_by = g1/right_hand
safe velocity and arm posture
replan around blocked route
abort if grip / balance uncertain
Notes: Now navigation starts a second, independent ROS action targeting the destination approach pose. Object stays attached to robot link, and original support relationship is removed. Carrying changes body envelope, dynamic constraints, safe gait/arm policy. If obstruction occurs, local route recovery may happen without task-level replan; if cup slips or collision risk increases, stop and escalate. G1 navigation interface still requires validated locomotion/WBC.

## Slide 18
G1 / EMBODIED SYSTEMS
SKILL 06 / VLA MANIPULATION
VLA PLACE — separate from arriving at the kitchen
The handoff is a manipulation goal, not an instruction to “walk and place.”
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
18
FIND
NAVIGATE
VLA PICK
NAVIGATE
VLA PLACE
VERIFY
DESTINATION EVIDENCE
target: kitchen_counter_02
place_zone: region_7
held_object: cup_17
verified_standing_pose: true
surface_clearance: valid
GR00T PLACE SKILL
Place on accessible surface
release under controlled posture
VERIFY INDEPENDENTLY
Object detached from hand
Cup supported by counter
Registry pose updated
Place task marked complete
Release issued is not sufficient: confirm the final support relation via fresh perception.
Notes: G1 finishes navigation to kitchen counter before switching to manipulation policy. Goal should contain object ID, destination geometry, target placement zone, contact constraints, camera frame, and timeout. Policy places then releases; independent perception verifies object support, no slipping/drop, hand detachment. Registry transitions from PLACE_PENDING to AVAILABLE at new location only after evidence.

## Slide 19
G1 / EMBODIED SYSTEMS
SKILL 07 / CLOSURE
Verify the goal, update memory, then report success
The world model is authoritative for semantic task state—not the VLA completion flag alone.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
19
TARGET
cup_17 exists in current scene
RELATION
ON_TOP_OF(cup_17, kitchen_counter_02)
ATTACHMENT
held_by = null
SAFETY
no collision / fall / unsafe release
SUCCESS = desired semantic state verified by current observations
Notes: An episode is complete if goal predicates satisfy the requested state, with fresh observations and no unresolved safety issue. Success metrics include actual object placement, no accidental disposal, stable final pose, and correct identity. Report pending/incomplete if camera cannot inspect final target, even if VLA returns done.

## Slide 20
G1 / EMBODIED SYSTEMS
CASE A / END-TO-END EXAMPLE
Red cup → kitchen counter: complete action trace
A useful regression test because it spans search, two navigation actions, and two VLA skills.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
20
1 PARSE
cup(red, on living_room_table) → kitchen_counter
2 FIND
memory miss → view table → detect cup_17
3 NAVIGATE
walk to reachable pose near cup_17
4 VLA PICK
grasp cup_17; verify ATTACHED
5 NAVIGATE
walk to kitchen while carrying cup_17
6 VLA PLACE
place on counter; release
7 VERIFY
cup_17 ON counter; update persistent DB
No step combines navigation and manipulation.
Notes: Sample trace is design illustration, not measured robot execution. Benchmark should log event IDs, pose transforms, object state, retry count, action results, last observation, costmap version and reference geometry for each step. Validate each transition independently.

## Slide 21
G1 / EMBODIED SYSTEMS
CASE B / TABLE CLEANUP
“Clean the table” can mean object removal—not wiping
Example: move a specifically designated disposable cup from the table into a trash bin.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
21
TABLE
DISPOSABLE CUP
TRASH
MISSION CONSTRAINTS
target = disposable_cup
support = table_03
destination = trash_bin_01
disposal permission required
verify bin contains target
This demonstrates pick-and-place cleanup, not surface wiping or sanitation.
Notes: If the user explicitly says put this cup in the trash, the planner can respect the instruction subject to robot safety and any household-level policy. If the instruction is only clean the table, do not infer every cup is trash. Classify disposable or request approval. The end-to-end task is object removal, not wiping, disinfection, dirt estimation, or autonomous waste sorting beyond supported skills.

## Slide 22
G1 / EMBODIED SYSTEMS
CASE B / ACTION SEQUENCE
Table cleanup still uses navigation and VLA as separate actions
Same seven-step contract, with a different destination and disposal gate.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
22
01
PARSE + AUTHORIZE
select cup eligible for disposal
02
FIND + GROUND
cup_23 ON table_03 confirmed
03
NAVIGATE 1
move to pickup pose beside table
04
VLA PICK
pick cup_23; confirm held_by G1
05
NAVIGATE 2
walk to trash_bin_01 while carrying
06
VLA PLACE
place cup into bin opening; release
07
VERIFY + UPDATE
cup_23 INSIDE bin; table clear
Place verification: cup is inside the bin, not on its rim, floor, or still in hand.
Notes: The trash example is deliberately handled as seven independent high-level skills. Active perception may need to find the bin as well as the cup, or use existing bin registry and fresh verification. The VLA PLACE skill should be trained for bin aperture and release, not just arbitrary counter placement. The robot must confirm disposal success with evidence, and avoid placing when the bin is full.

## Slide 23
G1 / EMBODIED SYSTEMS
CASE B / POLICY SAFETY
“Clean” is not permission to discard every object
The planner must distinguish disposable trash from reusable property and uncertain items.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
23
VISUAL CLASSIFICATION
Paper cup
Likely disposable
Ceramic mug
Reusable property
Unknown cup
Ambiguous
DECISION
AUTHORIZATION
Explicit or policy-approved
SAFE TO DISCARD?
yes / uncertain
OUTCOMES
YES
Execute nav / pick / nav / place
NO / UNKNOWN
Ask user or choose storage
In experiments, disposition classification and object identity errors count as safety failures.
Notes: Treat the instruction clean the table as underspecified. A reusable mug should not be thrown into a bin on an inferred policy. Require explicit disposal target or stored household rule; the user example of throwing a cup in trash should be treated as disposable or specifically authorized. In test scenarios, tag object truth labels; measure false disposal rate and uncertainty abstention.

## Slide 24
G1 / EMBODIED SYSTEMS
EXTENSION / ROOM TIDYING
Same interface scales to multiple objects and destinations
The planner loops over grounded objects; the underlying skill implementations remain unchanged.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
24
SEMANTIC TASK QUEUE
cup_23
paper cup
trash_bin_01
mug_08
ceramic mug
kitchen_counter
cloth_12
cleaning cloth
drawer_04
REPEATABLE LOOP
FIND / GROUND
NAVIGATE TO OBJECT
VLA PICK
NAVIGATE TO DEST
VLA PLACE
VERIFY & NEXT
Notes: Long-horizon cleaning means object inventory, destination assignment, ordering, repeated independent skill execution. Do not equate object relocation with full cleaning tasks such as wiping; that requires a separate trained tool-use skill. Task graph can optimize carrying, accessibility, priority, and retry budget. Agents should maintain goal predicates for each object.

## Slide 25
G1 / EMBODIED SYSTEMS
RECOVERY LOGIC
Failures should escalate to the smallest responsible agent
Use local recovery first; request mission-level replanning only when necessary.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
25
FAILURE EVENT
RECOVERY OWNER
CORRECT BEHAVIOR
Cup not visible
Active perception
new viewpoint / inspect table
Cup ambiguous
Grounding + planner
reobserve / ask user
Route blocked
Navigation
costmap replan / safe stop
Grasp failed
Manipulation
reobserve + bounded retry
Cup dropped
World + perception
mark LOST; re-localize
Trash bin full
Mission planner
alternate bin or report
Bound every retry with timeouts, attempt limits, fresh evidence, and an independent safety stop.
Notes: For unobservable cup, search next safe viewpoint. For ambiguous cup, do not choose one at random. For navigation blocked, Nav2 local recovery can replan. For failed grasp, VLA local bounded retry only after perception refresh. For drop, release attachment and re-ground identity. Bin full should trigger mission replan. Every recovery budget and action status must be logged.

## Slide 26
G1 / EMBODIED SYSTEMS
INTEGRATION / ROS 2
Three ROS 2 communication types, three purposes
Topics stream observations; services query memory; actions execute long-running skills.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
26
TOPICS
Stream, latest data
/perception/detections3d
/world/object_updates
/costmap /tf
SERVICES
Short query, reply
/world/find_objects
/world/get_object
/world/get_geometry_ref
ACTIONS
Goal, feedback, result
/perception/find_object
/nav/navigate_to_object
/vla/pick_object
/vla/place_object
Proposed interface names. ROS 2 Action result (SUCCEEDED/FAILED) must be observed before the next skill.
Notes: ROS 2 actions fit long-running active search, navigation and manipulation because they have Goal/Feedback/Result and cancellation. FindObjects is a fast world query service. Detections, tracked objects, TF2, costmap should be streamed. These names are proposals, not upstream published interface names. Standardize versions, map frame, timestamps, IDs, and terminal result codes.

## Slide 27
G1 / EMBODIED SYSTEMS
INTEGRATION / CONTRACTS
Use typed requests, IDs, and terminal results
Planner output is validated before any robot motion.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
27
FIND OBJECT / ACTION GOAL
{
"target": {"class": "cup",
"color": "red",
"support_id": "table_03"},
"max_viewpoints": 5,
"time_budget_s": 120,
"allow_navigation": true
}
FIND OBJECT / RESULT
{
"status": "FOUND",
"object_id": "cup_17",
"frame_id": "map",
"tracking_state": "CONFIRMED",
"evidence_timestamp": "...",
"pose": [2.4, 1.7, 0.82]
}
Example contracts, not API responses from an existing G1 integration.
Notes: Create .action files with explicit goal, feedback and result. Keep an object_id as a stable identifier and references into world state instead of repeating large geometry. Include `mission_id`, `event_id` and `schema_version` for tracking. Validate allowed skills, map frame, freshness, safety and authorization. Avoid LLM output directly becoming low-level torques or joint commands.

## Slide 28
G1 / EMBODIED SYSTEMS
IMPLEMENTATION / ALGORITHMS
Small deterministic managers around powerful models
Planning is replaceable; the validated skill interface remains constant.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
28
MISSION ORCHESTRATOR
plan = parse_and_validate(text)
obj = await find_object(plan.target)
assert obj.status == FOUND
await navigate(obj.pick_pose)
await vla_pick(obj.id)
assert registry.is_attached(obj.id)
await navigate(plan.destination)
await vla_place(obj.id, destination)
await verify_goal(plan)
ACTIVE PERCEPTION
candidates = world.query(target)
if fresh_match(candidates):
return verify(candidates)
views = plan_safe_views(target)
for view in views[:max_views]:
if await navigate(view) == SUCCESS:
world.update(await observe())
if grounded(target):
return FOUND(object_id)
return NOT_OBSERVED
Pseudocode: omitted real ROS 2 async state handling, cancellation, safety and timeout wiring.
Notes: Core logic is intentionally deterministic and testable; high-level model can propose a structured mission but it is not the authority on robot state. Active perception relies on safe views and budget. Real implementation needs ROS 2 action clients and server state handling, asynchronous cancellation, telemetry, persistence transaction boundaries, safety stops, and retry limits.

## Slide 29
G1 / EMBODIED SYSTEMS
DEPLOYMENT / LOCAL-FIRST
All runtime decisions can remain on your own machines
Codex is for software engineering—not the real-time control loop.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
29
DEV / RESEARCH PC
Codex CLI (subscription)
Source audits, code, reports
PLANNER GPU
Local RynnBrain / planner
Structured mission output
PERCEPTION + MAP
Existing 3D detection, scene
Costmap, world registry
VLA GPU
GR00T N1.7 fine-tuned
Policy inference
G1 / LOCAL CONTROL
ROS2 nav bridge + WBC
Safety, actuation, sensors
No external inference API in the robot runtime • Private LAN / authenticated RPC • Version-locked model checkpoints
Notes: This is a logical deployment partition, not a promise that each model fits a specific GPU. Profile VLM and GR00T GPU requirements, camera bandwidth, ROS2 DDS latency and network reliability. Original RynnBrain weights are available, but benchmark against fixed deterministic planner too. Codex subscription may assist software development but must not be used as the robot runtime planner. GR00T N1.7 G1 SONIC requires fine-tuned checkpoint as documented.

## Slide 30
G1 / EMBODIED SYSTEMS
VALIDATION / EXPERIMENTS
Benchmark perception, navigation, manipulation, and safety separately
A single end-to-end success rate cannot tell the team which component failed.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
30
FIND
Target recall / search success
views to find / false match
NAV
Goal success / path cost
blocked-route recovery
PICK
Grasp success / retries
attachment verification
PLACE
Target relation success
object drop / false success
MEMORY
ID switches / stale objects
correct state transitions
SAFETY
Collisions / falls / wrong disposal
unsafe action refusal
Start in deterministic skill simulation → Isaac Lab G1 physics → supervised real robot, after safety approval.
Notes: Proposed benchmark: first use oracle object and skill mocks to isolate planner, then closed loop physics with G1 and fixed low-level policies, then supervised hardware. Tasks: find cup, occluded cup, navigate pickup, pick, navigate while holding, place, room tidying, discard authorized cup. Stratify unseen layouts, illumination, dynamic obstacles, position noise, failed grasp, full bin. Report separate metrics with confidence intervals.

## Slide 31
G1 / EMBODIED SYSTEMS
ENGINEERING ROADMAP
Build in acceptance-gated milestones
Implement the semantic bridge first; integrate G1 motion only after simulation safety passes.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
31
M0
Interfaces & fixtures
Typed ROS2 contracts, TF2 frames, sample worlds
M1
Semantic memory
Stable object IDs, relations, persistence, queries
M2
Active perception
Viewpoint planning, grounded search, budgets
M3
Navigation
Nav2/G1 bridge, approach poses, feedback
M4
VLA skills
G1-trained N1.7 pick/place + state updates
M5
Full missions
Case A + B + recovery + held-out benchmark
Each milestone produces tests, logs, and explicit acceptance evidence before the next stage.
Notes: Milestones are logical rather than hard schedule promises: M0 contract design, M1 registry and persistence, M2 active perception using existing detector, M3 navigation using costmap and validated G1 controller, M4 fine-tuned GR00T N1.7 and state machine, M5 integration and benchmark. Codex can implement a phase only after approved design. Physical G1 motion always requires human authorization and safety review.

## Slide 32
G1 / EMBODIED SYSTEMS
SOURCES / BOUNDARIES
Upstream capabilities vs proposed G1 additions
The deck distinguishes demonstrated source behavior from a research implementation plan.
G1 SEMANTIC WORLD • PROPOSED RESEARCH DESIGN • OFFLINE-FIRST
32
Semantic-nav-amr
Memory/lookup + Nav2 object goal
Nav2 API
Goal / feedback / result contracts
ROS 2 Actions
Long-running skill semantics
vision_msgs
3D detector message conventions
Spark-DSG
Optional scene graph data structure
GR00T Whole-Body Control
G1 fine-tune + SONIC integration
Isaac Lab-Arena
G1 physics benchmark (published N1.6 example)
RynnBrain Plan
Local embodied task planner candidate
Full citations and links are included in slide notes. Source models and licences must be verified per deployment.
Notes: Primary source URLs: https://github.com/Gukdoli/Semantic-nav-amr ; https://docs.nav2.org ; https://design.ros2.org/articles/actions.html ; https://github.com/ros-perception/vision_msgs ; https://github.com/MIT-SPARK/Spark-DSG ; https://nvlabs.github.io/GR00T-WholeBodyControl/tutorials/vla_workflow.html ; https://github.com/isaac-sim/IsaacLab-Arena ; https://huggingface.co/Alibaba-DAMO-Academy/RynnBrain-Plan-8B . Note licensed components separately. All G1_semantic_world interface names and examples in deck are proposed, not existing upstream interfaces.